## Slide 1: Methanization (Anaerobic Digestion) and Biogas -Phase 1
Dr Charifi Samia
Université Mohamed Khider Biskra
Faculté SNVSTU
Département des Sciences de la nature et de vie
Niveau : Master Spécialité «Microbiolgie appliquée »
Année universitaire 2026/2027

## Slide 2
Improvement in the standard of living
Increased consumption
Changes in dietary habits
Food packaging
Organic waste
1.INTRODUCTION
Increasing energy needs
Agricultural activities
Animal waste: manure and slurry
Crop residues
Straw
Manure: a mixture of animal feces and bedding mate
Slurry: a liquid mixture of animal feces and water.
Fruit and vegetable waste

## Slide 3
Growth in waste production
Effective waste management policies
Encouraging sustainable practices
Biological processes for the treatment and valorization of organic matter

## Slide 4
I. Waste Valorization through Anaerobic Digestion
I.1. Waste Management
Waste management encompasses all operations involving
PART 1: WASTE VALORIZATION THROUGH ANAEROBIC DIGESTION
Prevention / Reduction at Source: Minimizing raw waste production.
Reuse: Finding direct secondary uses for materials.
Recycling & Material Recovery: Composting, structural recycling.
Energy Recovery: This is where biomethanation sits,
Disposal: Landfilling or incineration without energy capture (last resort).

## Slide 5
Definition of Methanogenic Waste and Effluents
These wastes represent a valuable source of organic matter that can be converted into biogas, mainly Methane (CH₄).
This organic matter is found in various sources, ranging from municipal waste to industrial effluents, including sewage sludge.

## Slide 6
Classification by Origin:
Household and municipal waste:Household biowaste (food scraps, fruit and vegetable peelings).
Agricultural Residues:ivestock manure: slurry and solid manure (rich in nitrogen and microorganisms). Crop residues (straw, corn stalks)
Agri-food and industrial waste:
(slaughterhouse by-products, Lactosérum
Urban waste and wastewater treatment plant (WWTP) sludge:
sludge generated during wastewater treatment.
I.2.1 Main Types of Waste Concerned
The available feedstock corresponds to the biodegradable fraction of waste (biodegradable organic fraction)

## Slide 7
How Do Microorganisms Obtain Energy?
The key question: Who accepts the electrons?
ORGANIC MATTER
e⁻
Who receives the electrons?
The final electron acceptor determines the metabolic pathway.

## Slide 8
1. Aerobic Respiration
Oxygen is available
ORGANIC MATTER
e⁻
H₂O
Organic matter + O₂ → CO₂ + H₂O + energy
O₂ = final electron acceptor

## Slide 9
2. Anaerobic Respiration
No free oxygen: another electron acceptor is used
ELECTRON DONOR
e⁻
NO₃⁻
SO₄²⁻
CO₂
N₂
H₂S
CH₄
NO₃⁻ → N₂ | SO₄²⁻ → H₂S | CO₂ → CH₄

## Slide 10
FERMENTATION
ORGANIC MATTER
NO O₂ + NO EXTERNAL ELECTRON ACCEPTOR
The organic substrate provides both the electron donor
and the electron acceptor.

## Slide 11
ALCOHOLIC FERMENTATION
Glucose → ethanol + CO₂
GLUCOSE C₆H₁₂O₆
ETHANOL C₂H₅OH
CO₂
C₆H₁₂O₆ → 2 C₂H₅OH + 2 CO₂ + energy
Main products: ethanol and carbon dioxide.

## Slide 12
LACTIC FERMENTATION
Glucose → lactate
GLUCOSE
LACTATE C₃H₅O₃⁻
C₆H₁₂O₆ → 2 C₃H₆O₃ + energy
Lactic fermentation produces mainly lactate (lactic acid in its protonated form.

## Slide 13
BUTYRIC FERMENTATION
An example of acid fermentation
GLUCOSE
BUTYRATE
H₂
CO₂
C₆H₁₂O₆ → C₄H₈O₂ + 2 CO₂ + 2 H₂
Fermentation pathways vary with microorganisms and environmental conditions.

## Slide 14
The Key Idea to Remember
AEROBIC
O₂ → H₂O
ANAEROBIC RESPIRATION
NO₃⁻ → N₂ SO₄²⁻ → H₂S CO₂ → CH₄
FERMENTATION
No external electron
acceptor
The key question is: What is the final electron acceptor?

## Slide 15
Energy Metabolisms and Their Practical Implications:
The biological degradation of organic matter is a metabolic oxidation–reduction (redox) reaction.
Microorganisms obtain energy by transferring electrons from organic matter to an electron acceptor. The nature of the final electron acceptor determines the metabolic pathway:
Aerobic metabolism: the final electron acceptor is molecular oxygen (O₂).
Anaerobic metabolism: the final electron acceptor is a mineral compound other than oxygen (such as NO₃⁻ or SO₄²⁻) or, in fermentation, an organic molecule derived from the substrate itself.

## Slide 16
Procédé aérobie
Aerobic Respiration: Oxygen (O2) acts as the final electron acceptor. It produces CO2, water (H2O), and a high amount of energy (ATP), leading to significant cellular biomass production (e.g., composting). C₆H₁₂O₆ + 6 O₂ → 6 CO₂ + 6 H₂O + energy

## Slide 17
Procédé aérobie
Energy yield: High. approximately 30–32 ATP molecules per glucose molecule .
High biomass production: A significant fraction of the organic carbon is incorporated into new microbial biomass, generating excess biomass or sludge.
High heat production: Aerobic degradation is strongly exothermic. This heat generation is fundamental to composting, where temperatures can rise to approximately 50–70°C, contributing to the hygienization of the material.
Need for aeration: Continuous or periodic oxygen supply is required, which may involve significant energy consumption for forced aeration, turning, or mixing.
Final products: Mainly CO₂, H₂O, microbial biomass, and, in composting, stabilized organic matter (compost)

## Slide 18
I.2.2.3 Anaerobic Respiration and Fermentation
In the absence of free oxygen (O₂), microorganisms can degrade organic matter through different anaerobic pathways, mainly anaerobic respiration and fermentation.
1. Anaerobic Respiration External Mineral Electron Acceptor
In anaerobic respiration, the final electron acceptor is a mineral compound other than oxygen.
Examples include:
Denitrification: nitrate (NO₃⁻) acts as the electron acceptor and is ultimately reduced to gaseous nitrogen (N₂).
Sulfate reduction: sulfate (SO₄²⁻) is reduced, producing hydrogen sulfide (H₂S).
Methanogenesis: in hydrogenotrophic methanogenesis, CO₂ acts as an electron acceptor and is reduced to CH₄:

## Slide 19
Anaerobic Respiration and Fermentation
Occurs in the complete absence of oxygen (O2). Electron acceptors are inorganic compounds (NO3- SO4 2-, CO2) or organic molecules. Energy yield is lower, generating methane (CH4), CO2, and a small amount of residual biomass.

## Slide 20
Low energy yield for microorganisms: Anaerobic metabolism generally provides less usable energy for microbial growth than aerobic respiration.
Lower biomass production: Because less energy is available for growth, anaerobic processes generally produce less excess microbial biomass than aerobic treatment.
Energy conservation in methane: A substantial portion of the chemical energy originally contained in the organic matter remains stored in the reduced methane molecule CH₄.
Biogas production: Anaerobic digestion produces biogas, mainly composed of CH₄ and CO₂, with smaller quantities of H₂S, H₂, NH₃ and water vapor, depending on the substrate and operating conditions.
Digestate production: The process also produces digestate, which contains stabilized organic matter and nutrients and can potentially be used as a soil amendment or fertilizer, subject to appropriate quality and safety requirements.
Technological and Operational Implications for Anaerobic Digestion

## Slide 21
Influence of the Medium Composition on Anaerobic Metabolism
1. If the medium is anaerobic or anoxic and contains nitrate (NO₃⁻), certain microorganisms can use nitrate as the final electron acceptor.
NO₃⁻ → NO₂⁻ → N₂
This process is called denitrification and product is nitrogen gas (N₂),
2. If the anaerobic medium contains sulfate (SO₄²⁻), certain microorganisms can use sulfate as the final electron acceptor:
SO₄²⁻ → H₂S / HS⁻
This process is called sulfate reduction and product is hydrogen sulfide (H₂S),
The microorganisms involved are called sulfate-reducing microorganisms.
3. Methanogenesis requires strictly anaerobic conditions Methanogenic archaea use different substrates, mainly H₂/CO₂
One of the main reactions is:
CO₂ + 4 H₂ → CH₄ + 2 H₂O
Therefore, the composition of the medium strongly influences the metabolic pathways that can occur.
Anaerobic medium + NO₃⁻ → denitrification → N₂
Anaerobic medium + SO₄²⁻ → sulfate reduction → H₂S
Favorable anaerobic conditions + CO₂/H₂ → methanogenesis → CH₄

## Slide 22
Criterion | Aerobic pathway (e.g., composting) | Anaerobic pathway (e.g., anaerobic digestion)
Electron acceptor | O₂ | NO₃⁻, SO₄²⁻, CO₂, or organic compounds depending on the pathway
Energy available to microorganisms | Generally high | Generally lower
Biomass production | Relatively high | Relatively low
Main products | CO₂ + H₂O + biomass | CH₄ + CO₂ + digestate
Energy recovery | Mainly dissipated as heat | Energy retained in methane and recoverable as biogas
Oxygen requirement | Required | No free oxygen
Main infrastructure | Aeration and/or turning systems | Airtight anaerobic digesters and gas collection systems
Main application | Composting and aerobic biological treatment | Biogas production and digestat

## Slide 23
Critères | Description of Anaerobic Process | Description of Aerobic Process
Energy efficiency | Efficient conversion of waste into biogas | Energy consumption for aeration
Waste reduction | Significant reduction of organic waste | Efficient degradation of organic matter
Operational costs | Complex installation | Relatively simple technical means
Environmental sustainability | Global environmental impact | Global environmental impact
Production | Quantity and quality of biogas; digestate | Compost production
Residues | Quality of solid residue after digestion | Elimination of pollutants in the effluent
++
++
++
++
++
++
++
++